## Slide 1: Introduction to Network Traffic Analysis
Stephen Deck, GSE, OSCE, CISSP
BE INFORMED. BE STRATEGIC. BE SECURE.
Notes: Goal is to have a decent understanding of the basics and be able to do something useful

## Slide 2: Overview
Part 1: The Basics
Part 2: Tools
Part 3: Common Protocols
Part 4: Scapy
Part 5: Analysis Tips
Part 6: Practical Exercise

## Slide 3
Part 1 – The Basics

## Slide 4: Overview Part 1 – The Basics
OSI & TCP/IP Model Overview
Hexadecimal Numbers
Binary Numbers
Ethernet Headers
IP Headers
TCP Headers
UDP Headers
ICMP Headers

## Slide 5: Why Bother with Packet Analysis?
Faster than host-based forensics
Investigate networking alerts
Troubleshoot networking issues
Tell if tools are working
Reverse engineer protocols
Notes: Blue team
Engineering
Application testing

## Slide 6: The OSI Model
7. Application
6. Presentation
5. Session
4. Transport
3. Network
2. Data Link
1. Physical
Notes: Was the de facto model until recently
Still used by many
Consistent references to “Layer 8” problems
Being replaced by TCP/IP model

## Slide 7: The TCP/IP Model
7. Application
6. Presentation
5. Session
4. Transport
3. Network
2. Data Link
1. Physical
4. Application
3. Transport
2. Internet
1. Network Access
Notes: TCP/IP along-side the OSI model
Much simpler representation
-doesn’t help with ideas like SSL/TLS
Will try to remember to use the TCP/IP model in references

## Slide 8: Encapsulation
Example encapsulated HTTP request
Notes: Encapsulation is going down the stack
Decapsulation is going back up
The payload and header of one level becomes the payload of the next lower level

## Slide 9: Decimal in a New Light
8080
100 = 1
101 = 10
102 = 100
103 = 1000
104 = 10000
103 | 102 | 101 | 100
Notes: Can’t move on to headers without understanding binary and hex numbers
Rarely need to go over 65535
Decimal can help make sense of hex and binary
Each column is just a base 10 power

## Slide 10: Hexadecimal Numbers
Base 16 (normal counting is decimal, base 10)
Decimal to Hex : Divide by powers of 16, ignore remainders
Hex to Decimal : Multiply by powers of 16
Prefixed by 0x
Notes: Hex to decimal and vice versa is a pain.
Decimal to hex, lots of divide, subtract, repeat
Hex to decimal is not so bad. Multiply each column by its power of 16

## Slide 11: Counting in Hex
Decimal | Hex
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
6 | 6
7 | 7
8 | 8
Decimal | Hex
9 | 9
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F
16 | 10
Notes: More than 10 numbers. Arabic numerals (decimal) has 10
Use alphabet A-F to make up the difference
After F, start over at 1-0

## Slide 12: Decimal to Hex Conversion
8080/4096 = 1.xxxx
8080-(4096*1) = 3984
3984/256 = 15.xxxx
3984-(15*256) = 144
144/16 = 9.0
160 = 1
161 = 16
162 = 256
163 = 4096
164 = 65536
1 F 9 0
163| 162 | 161 | 160
Notes: Commit powers of 2 and 16 to memory
Start with biggest power of 16, divide.
Subtract that power from the value
Repeat

## Slide 13: Hex to Decimal Conversion
160 = 1
161 = 16
162 = 256
163 = 4096
164 = 65536
1 F 9 0
163| 162 | 161 | 160
1(4096) + 15(256) + 9(16) + 0(1) = ?
4096+3840+144+0 = 8080
Notes: Hex to decimal is straight multiplication by powers
Again, know the powers of 2 and 16 cold

## Slide 14: Binary Numbers
Base 2
Decimal to Binary : Divide by powers of 2, ignore remainders
Binary to Decimal : Multiply by powers of 2
Hex to Binary : Direct conversion of bytes to bits
Binary to Hex : Direct conversion of bits to bytes
Notes: Binary is the same. Just powers of 2
Never convert decimal to binary.
Use hex as an intermediate step.
Converting hex to binary is just converting bytes to bits
What does that mean?

## Slide 15: Bits, Bytes, and Nibbles
A bit is a single binary number, 1 or 0
A byte is 8 bits
A nibble is 4 bits
Notes: Just normal terminology.
A bit is just a single pulse of electricity, a high or low voltage
Foundation of computing and data transfer

## Slide 16: Counting in Binary
Decimal | Hex | Binary
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
Decimal | Hex | Binary
9 | 9 | 1001
10 | A | 1010
11 | B | 1011
12 | C | 1100
13 | D | 1101
14 | E | 1110
15 | F | 1111
16 | 10 | 00010000
Notes: Binary counting is awkward at first
Kind of calm and relaxing
Mostly memorize 0-F conversions

## Slide 17: Hex to Binary
1F90=
0001 1111 1001 0000
1 = 0001
F = 1111
9 = 1001
0 = 0000
Notes: Simple. Convert the numbers from hex to binary and concatenate

## Slide 18: Hex Bytes and Nibbles
Nibble is a single hex digit
Byte is two hex digits
Notes: Important for packet headers and addressing

## Slide 19: Words
A word is 2 bytes (16 bits)
A double-word is 4 bytes (32 bits)
Often done in hex
Notes: Common in memory addressing
Sometimes useful in packet headers
Values like ports and IP addresses

## Slide 20: Knowledge Check
Convert CAFE to decimal
Convert 7A69 to binary
  What is the high order nibble of the low order byte in binary?
  What is the low order nibble of the high order byte in hex?

## Slide 21: Knowledge Check - Answers
Convert CAFE to decimal – C=12, A=10, F=15, E=14
12(163)+10(162)+15(161)+14(160) =
12*4096+10*256+15*16+14 = 51966
Convert 7A69 to binary – 0111 1010 0110 1001
  What is the high order nibble of the low order byte in binary?
  0110
  What is the low order nibble of the high order byte in hex?
  A

## Slide 22: Network Access Layer
Common protocols: Ethernet, Wireless, Bluetooth
Ethernet & Wireless use Media Access Control (MAC) addresses
Information does not “route”

## Slide 23: Ethernet Headers – Network Access Layer
Source: https://en.wikipedia.org/wiki/Ethernet_frame
Notes: Not relevant in most forensics, most attacks, or most engineering issues

## Slide 24: Internet Layer – IPv4
Routes packets across the internet
Uses 32-bit IP addresses
ARP resolves MAC to IP
Header length depends on options
  Not that common
Does not guarantee delivery

## Slide 25: IPv4 Header – Internet Layer
http://wiki.gnhlug.org/twiki2/pub/Www/IpReference/Packet_Headers_Subnet_Breakdown.xls
Notes: Mention fragmentation – covering if time permits
IP header length multiplied by 4 for length in bytes
Type of Service – aka differentiated services for ECN
TTL Router that changes it to 0 discards
Protocol field – determines transport-layer protocol
IP options – not common
Checksum just detects corruption – not discussing

## Slide 26: IPv4 Fragmentation
Naturally occurs
  Packet size exceeds MTU (Maximum Transmission Unit)
Sometimes orgs block it
Foundation for many bypass techniques
Observation point and target must decode the same way
RFCs do not deal with edge cases

## Slide 27: IPv4 Fragmentation
Fragments are in IP header, bytes 6 and 7
DF – Don’t Fragment
MF – More Fragments
Multiply fragment offset by 8, 13 bits cannot represent full packet length
MF bit set when more fragments follow (not in last frag or unfragmented packets)

## Slide 28: IPv4 Fragmentation – Example (icmpfrag.pcap)
Payload per packet size = MTU-(IP header length)
Only first packet in the train has the transport protocol header
MTU of 1500 (Ethernet)
20 byte IP header
1480 payload bytes per packet
Packet 1 Offset : 0
Packet 2 Offset : 1480/8 decimal = B9 hex
Packet 3 Offset : 2960/8 decimal = 172 hex

## Slide 29: IPv4 Fragmentation - Insertion
Observation system accepts data the target does not
Attacker
Observer
Target
cat /etc/
derp
shadow
cat /etc/derpshadow
cat /etc/shadow
cat /etc/
derp
shadow

## Slide 30: IPv4 Fragmentation - Evasion
Observation system rejects data the target does not
Attacker
Observer
Target
cat /etc/
shadow
cat /etc/
shadow
cat /etc/
cat /etc/shadow

## Slide 31: Traceroute
Find list of hops between hosts
Relies on ICMP Time Exceeded in Transit messages
Can use ANY layer 4 protocol
Send packets with variable TTL values
Each hop decrements TTL by 1, discarding router sends ICMP
Windows uses ICMP echo requests
Linux uses UDP 33434 to UDP 33534
Notes: SYN with no response means blocked (firewall, IPS?)

## Slide 32: Internet Layer – IPv6
Same purpose as IPv4
Uses 128-bit IP addresses
Neighbor Solicitation resolves MAC to IP
Does not guarantee delivery

## Slide 33: IPv6 Header – Internet Layer
https://www.cisco.com/c/en/us/about/security-center/countermeasures-ipv6-type-0.html

## Slide 34: Transport Layer - TCP
Transmission Control Protocol
Ensures packet delivery
Most common transport layer protocol
Communication status controlled with TCP flags

## Slide 35: TCP Header
http://wiki.gnhlug.org/twiki2/pub/Www/IpReference/Packet_Headers_Subnet_Breakdown.xls
Notes: Cover TCP flags
Mention TCP Options
Sequence number controls which conversation
Acknowledgement number controls where we are in conversation

## Slide 36: TCP Conversations - Beginning
Client
Server
SYN
SYN - ACK
ACK

## Slide 37: TCP Conversations - Ending
?
RST
FIN-ACK
FIN - ACK
?
?
?
?

## Slide 38: TCP - Tracking Conversations
Socket (Source – Destination combination)
Sequence Number
  Client and server have different sequence numbers
Acknowledgement Number
  Acknowledge last sequence # + payload length
Wireshark tracks this well

## Slide 39: TCP - Tracking Conversations
C-S – Syn – SEQ 0x82acd14d ACK 0x00000000, no payload
S-C – Syn-Ack – SEQ 0x9696fd7e ACK 0x82acd14e, no payload
C-S – Ack – SEQ 0x82acd14e ACK 0x9696fd7f, no payload
C-S – Ack – SEQ 0x82acd14e ACK 0x9696fd7f, 306 byte payload
S-C – Ack – SEQ 0x9696fd7f ACK 0x82acd280, no payload
S-C – Ack – SEQ 0x9696fd7f ACK 0x82acd280, 1261 byte payload
C-S – Ack – SEQ 0x82acd280 ACK 0x9697026c, 286 byte payload
S-C – Ack – SEQ 0x9697026c ACK 0x82acd39e, 1460 byte payload

## Slide 40: TCP - Retransmission
Blocked connections usually reset or dropped
Dropped packets look “lost” to host
Hosts retry at progressively larger intervals
Notes: Important for scanning and troubleshooting

## Slide 41: TCP - Retransmission

## Slide 42: TCP – “Normal” Behavior
SYN to an open port causes SYN-ACK response
SYN to a closed port causes a RST
Notes: SYN with no response means blocked (firewall, IPS?)

## Slide 43: Transport Layer - UDP
User Datagram Protocol
Unreliable delivery
Faster than TCP
Packet loss handled at the application layer
Suitable for streaming (VOIP, video, etc)
DNS and tftp commonly use UDP
QUIC uses UDP
Notes: Good that IP is unreliable, so it supports UDP

## Slide 44: UDP Header
http://wiki.gnhlug.org/twiki2/pub/Www/IpReference/Packet_Headers_Subnet_Breakdown.xls

## Slide 45: Transport Layer - ICMP
Internet Control Message Protocol
Administrative communication
Ping, unreachable messages, router advertisement, redirection, etc.
Often result from a stimulus
  Ping response
  Port unreachable

## Slide 46: ICMP Header
http://wiki.gnhlug.org/twiki2/pub/Www/IpReference/Packet_Headers_Subnet_Breakdown.xls

## Slide 47: ICMP Header
http://slideplayer.com/slide/6252793/

## Slide 48: ICMP Anomalous Traffic
Response with no stimulus
  ICMP echo responses with no request
  Different numbers of ICMP echo requests and responses
  Nonstandard payloads
    Windows echo request abcdefghijklmnopqrstuvwabcdefghi
    Linux echo request !"#$%&'()*+,-./01234567

## Slide 49: ICMP Tunnel

## Slide 50: Transport Layer – ICMPv6
Internet Control Message Protocol
Same purpose as ICMPv4
Additional responsibility – Neighbor Discovery Protocol

## Slide 51: Knowledge Check
What ICMP type and code indicate a ping response?
What two bytes start most IPv4 packets?
What ICMP type might indicate a traceroute?
What are the steps to the TCP 3-way handshake?
What are the two common methods of terminating a TCP connection?

## Slide 52: Knowledge Check
What ICMP type and code indicate a ping response?
  Type 0, code 0
What two bytes start most IPv4 packets?
  0x4500
What ICMP type might indicate a traceroute?
  Type 11
What are the sets of flags in a normal TCP 3-way handshake?
  SYN, SYN-ACK, ACK
What are the two common methods of terminating a TCP connection?
  FIN, RST

## Slide 53
Part 2 – Tools

## Slide 54: Overview Part 2 – Tools
TCPDump
Wireshark
TShark
ngrep
GNU Tools

## Slide 55: TCPDump
Packet sniffing application
*nix, windump on Windows
Little interpretation past transport layer
Fastest sniffer available
Uses Berkeley Packet Filters (BPF)

## Slide 56: TCPDump Common Options
-nn : Do not resolve host names or ports
-i : Capture interface
-w : write packets to a file
-r : read capture file
-A : Dump ASCII
-x : Dump hex
-X : Dump hex and ASCII
-v[vvvv] : increase verbosity

## Slide 57: TCPDump
Notes: Ack packet shows up as a . In TCP flags!

## Slide 58: TCPDump Verbose Output

## Slide 59: Berkeley Packet Filters
Widely used in networking tools
Limit traffic TCPDump accepts
Allows targeted captures
Filter existing captures

## Slide 60: Berkeley Packet Filters
host host : capture traffic from a specific host
src host host : specific source host
dst host host : specific destination host
ip src host host : IP packets from specific source host
Port port : Packets to or from a specific transport-layer port
ether ehost : packets from a specific MAC
net subnet : packets to or form a specific subnet

## Slide 61: Berkeley Packet Filters
ip[0] = 0x45 : IPv4 packets, header length 20
tcp[2:2] = 443 : TCP packets destination port 443
tcp : capture all TCP packets
udp : capture all UDP packets
tcp && src host host : TCP packets from a specific host
tcp || src host host : Any TCP packet or packet from a specific host

## Slide 62: TCP Flags (Byte 13)
Byte 13 in the TCP header contains control flags
Help manage the TCP conversation

## Slide 63: Berkeley Packet Filters
tcp[13] = 0x02 : SYN packets
tcp[13] = 0x04 : RST packets
tcp[tcpflags] = tcp-syn : also SYN packets
How can you capture packets without the SYN flag set?

## Slide 64: Bit Masking
Logical AND (&)
  Both statements must be true
Logical OR (|)
  Either statement is true

## Slide 65: Berkeley Packet Filters
Packets with the SYN flag set
tcp[13] & 0x02 == 0x02

## Slide 66: Berkeley Packet Filters
Packets without the SYN flag set
tcp[13] & 0x02 != 0x02
tcp[13] & 0x02 = 0

## Slide 67: Knowledge Check
Find SYN-ACK packets
Find packets with a source port of 80
Find packets with all TCP flags set
Find all UDP packets with a destination port of 123
Find all type 3 code 3 ICMP packets

## Slide 68: Knowledge Check Answers
Find SYN-ACK packets
  tcp[13]=0x12
Find packets with a source port of 80
  src port 80
  udp[0:2]=80 || tcp[0:2]=80
Find packets with all TCP flags set
  tcp[13]=0xff
Find all UDP packets with a destination port of 123
  udp[2:2]=123
  udp && dst port 123
Find all type 3 code 3 ICMP packets
  icmp[0]=3 && icmp[1]=3

## Slide 69: Wireshark
Not as confusing as TCPDump
Graphical interface to view packets
Robust application layer support
More powerful filters
Slow.
Can be misleading
Almost unusable > 1GB packet captures
Can have remote code execution vulnerabilities

## Slide 70: Wireshark – Time Display

## Slide 71: Wireshark

## Slide 72: Wireshark Statistics

## Slide 73: Wireshark Exports
Dump files from pcaps
File | Export Objects
Limited protocol support
  HTTP
  SMB
  DICOM
  IMF
  TFTP

## Slide 74: Export Objects

## Slide 75: Wireshark Follow TCP Streams
Limits displayed packets to a specific set
Can use to export alternate protocols

## Slide 76: Followed TCP Stream - HTTP

## Slide 77: Followed TCP Stream - SMB

## Slide 78: Wireshark Filters
Capture Filters
  Use BPF to limit traffic collected
Display Filters - SLOW
  Wireshark-specific language
  Limit traffic displayed
  Does not alter capture file
  Intellisense

## Slide 79: Wireshark Display Filters
Equality & comparison
  Numeric : ==, !=, <, <>, >, <=, >=
  String : eq, ne, lt, gt, le, ge
  contains
  matches
Logical operators
  &&, ||, !
  and, or, not
Parenthetical notation
  Use parenthesis to group logic statements

## Slide 80: Common Wireshark Display Filters
ip.addr == host
ip.src == host
http.request.full_uri contains “string”
ip.addr == host && (dns || http.request.full_uri || ssl.handshake.certificate)
tcp.port == port
!(ip.addr == host)

## Slide 81: Display Filters Interface
Working filter
Broken filter
Insane filter

## Slide 82: TShark
Command line interface to Wireshark
Supports display filters
Far faster
Supports file exports (recent versions)
Parse with text-based tools
Slower than tcpdump, but more functional

## Slide 83: TShark Command Line Switches
-r : read pcap file
-nn : do not resolve ports and hosts
-Y : display filter
-T : format output
-e : specify fields
-w : write packets to file
--export-objects : export objects of specified protocol to specified directory

## Slide 84: TShark Command Line Switches

## Slide 85: TShark Command Line Switches

## Slide 86: TShark Output Fields
Separate multiple fields into separate –e arguments
  tshark -r filename.pcap -T fields -e 'http.request.full_uri' -e 'http.referer' -Y 'tcp.port==80’
I would not call it complete…
  Some fields are blank for no reason
List of all possible fields
  https://www.wireshark.org/docs/dfref/
  icmp.data
  http.request.full_uri
  http.referer

## Slide 87: Ngrep
Find packets matching a regex
grep, but for packets
Why not use grep?
  Need to know the packet information
Command line switches
  -qI : suppress hash marks, read from file

## Slide 88: Ngrep

## Slide 89: Text Parsing
Find, massage, and present text
One of the best skills to have
Not just for packet analysis
Linux-based tools
  Also have windows versions

## Slide 90: Output Redirection
stdin, stdout, stderr
| : direct stdout to stdin
> : direct stdout to file
>> : direct stdout append to file
< : direct file to stdin
2>&1 : direct stderr to stdout

## Slide 91: Cut
Splits input into columns
Outputs selected columns
Bad for reordering
Splits on arbitrary characters
Beware of repeating characters
Switches
  -f field_number : select specified fields
  -d ‘delimiter’ : use specified delimiter to split

## Slide 92: Cut
Notes: Run without cut
tshark -r 2018-01-16-traffic-analysis-exercise.pcap -nn -Y 'http' 2>&1 | cut -f7 -d’ ‘
Spaces in output

## Slide 93: Translate - tr
Replaces single character
tr ‘a’ ‘b’ : replace a with b
tr -s ‘ ‘ : squeeze repeating characters
tr -d ‘:‘ : delete character
Very handy before cut

## Slide 94: Tr with Cut

## Slide 95: Cut Multiple Columns
cut -f5,7-8,10- -d’ ‘
cut columns 5, 7 through 8, 10, and all columns after 10, delimited by space

## Slide 96: Sort
Orders text
Alphabetical or numeric
  -n : numeric sort
Can reverse sort
  -r : reverse sort
Needed for aggregation

## Slide 97: Output Chain
| tr -s ' ' | cut -f5 -d' ' | cut -f5 -d'.' | tr -d ':' | sort
Squeeze spaces
Get column 5, space delimited
Get column 5, period delimited
Delete the : character
Sort output

## Slide 98: Unique - uniq
Aggregates repeating lines
Can provide a count with –c
Sort first

## Slide 99: Get Top 10 Destination Ports

## Slide 100: Head & Tail
head -n number
  Get top number rows (default 10)
tail -n number
  Get last number rows (default 10)

## Slide 101: Get Top 10 Destination Ports – New Connections

## Slide 102: Word / Line Count
wc
wc -l
  Count lines
Answer “how many ports” and “how many hosts” questions

## Slide 103: Decoding
xxd
  Decode ASCII to hex and hex to ASCII
  xxd -r -p
    Hex to ASCII
Base64
  Encode/decode base64 encoded content
  Decode: base64 -d
  Encode: base64 -e

## Slide 104: Practical Exercise - Fragmentation
frags.pcap
  Why might only 1 host have responded to the ICMP echo request?
frags2.pcap
  What was the server’s response code?
  What URL was probably requested?

## Slide 105: Practical Exercise - Scanning
nmap.pcap
  Which host was performing scanning?
  Which host was the scan target?
  How many TCP ports were scanned?
  How many UDP ports were scanned?
  Which TCP ports were open?
  What may have caused the scan behavior after 12:04:10?

## Slide 106: Practical Exercise – Fragmentation Answers
frags.pcap
  Why might only 1 host have responded to the ICMP echo request?
    Fragmented ICMP blocked by Google, but not by local router
frags2.pcap
  What was the server’s response code?
    301
  What URL was probably requested?
    www.google.com

## Slide 107: Practical Exercise – Scanning Answers
nmap.pcap
  Which host was performing scanning?
    192.168.2.175
    tcpdump -r nmap.pcap -nn 'tcp[13]=0x02' | cut -f3 -d' ' | cut -f1-4 -d '.' | sort | uniq -c | sort -n

## Slide 108: Practical Exercise – Scanning Answers
nmap.pcap
  Which host was the scan target?
    192.168.2.75
    tcpdump -r nmap.pcap -nn 'tcp[13]=0x02' | cut -f5 -d' ' | cut -f1-4 -d '.' | sort | uniq -c | sort –n

## Slide 109: Practical Exercise – Scanning Answers
nmap.pcap
  How many TCP ports were scanned?
    1000
    sudo tcpdump -r nmap.pcap -nn 'tcp[13]=0x02 && src host 192.168.2.175 && dst host 192.168.2.75'| cut -f 5 -d' ' | cut -f5 -d'.'| cut -f1 -d':' | sort | uniq | wc –l
  How many UDP ports were scanned?
    30
    sudo tcpdump -r nmap.pcap -nn 'udp && src host 192.168.2.175 && dst host 192.168.2.75'| cut -f 5 -d' ' | cut -f5 -d'.'| cut -f1 -d':' | sort | uniq | wc -l

## Slide 110: Practical Exercise – Scanning Answers
nmap.pcap
  Which TCP ports were open?
    1025,1026,1027,1031,1032,1034,135,139,2869,3306,445,5357
    sudo tcpdump -r nmap.pcap -nn 'tcp[13]=0x12 && dst host 192.168.2.175 && src host 192.168.2.75'| cut -f 3 -d' ' | cut -f5 -d'.'| cut -f1 -d':' | sort | uniq

## Slide 111: Practical Exercise – Scanning Answers
nmap.pcap
  What may have caused the scan behavior after 12:04:10?
  Firewall enabled that does not reset connections

## Slide 112
Part 3 – Common Protocols

## Slide 113: Overview Part 3 – Common Protocols
HTTP
SSL
ARP (not app layer)
DNS
FTP

## Slide 114: HTTP
Extremely common
Source of most infections
Often permitted through firewalls
Use 2015-08-31-traffic-analysis-exercise.pcap for examples (from malware-traffic-analysis.net)

## Slide 115: HTTP Request

## Slide 116: HTTP Response

## Slide 117: Important HTTP Response Headers
“Referer”
  Tells which page caused the current request
  May be blank if referred from HTTP to HTTPS
Location
  30X responses send user to “Location” header value
Content-Type
  Tells how to interpret server response

## Slide 118: HTTP Redirection
Only certain ways to load content
  30X response code
  iframe
  script
  meta refresh
http://ranger-cha.blogspot.com/2015/02/following-trail-http-referer-header.html

## Slide 119: HTTP Forensics
Starting from an alert…

## Slide 120: HTTP Forensics
Use source port

## Slide 121: HTTP Forensics
Follow TCP stream

## Slide 122: HTTP Forensics
Find iframe

## Slide 123: HTTP Forensics

## Slide 124: HTTP Forensics

## Slide 125: HTTP Forensics
After finding the exploit, work backwards from the alert

## Slide 126: HTTP Forensics

## Slide 127: HTTP Forensics
What happened?
  User went to google
  Clicked on a link
  web.feeddigest.com
  302 redirect to vitaminsthatrock.com
  iframe to vclphjybj.ioxbpjgtqvwqfzmwhn.ga:13390
  Loaded flash exploit

## Slide 128: HTTP Forensics
Why bother?
  Effective blocks
  Supply malware analysis teams
  Effective threat intelligence
  Build statistics
  Notify compromised sites

## Slide 129: SSL
Becoming more common
Uses public key infrastructure (PKI)
Encrypts other protocols (often HTTP)
Can authenticate the client, but not common
Often permitted through firewalls
ssl_pcap_example.pcap

## Slide 130: SSL Connection Steps
TCP handshake
Client hello (supported protocols & cipher suites)
Server cert & key exchange (selected protocol & cipher suite)
Client session key & change cipher spec

## Slide 131: SSL Handshake in Wireshark

## Slide 132: SSL – What do we know?
Client supported protocols and cipher suites
  Client public key if used
Server selected protocol and cipher suite
Server public certificate
  May have site name in cert

## Slide 133: SSL Decryption
Need to decrypt the session key
Does not work with Diffie-Hellman key exchange
Client encryption info is ephemeral
  Can enable SSL key logging in browser
Server private key can decrypt

## Slide 134: SSL Decryption

## Slide 135: SSL Decryption

## Slide 136: Address Resolution Protocol (ARP)
Resolve MAC address to IP address
Stays within broadcast domain
Request and response packets
No security
  Allows MitM

## Slide 137: Address Resolution Protocol (ARP) Format
Hardware Type (Word)
Protocol Type (Word)
Hardware Size
(Byte)
Protocol Size
(Byte)
Opcode
(Word)
Sender MAC
(6 Bytes)
Sender IP
(4 Bytes)
Target
MAC
(6 Bytes)
Target IP
(4 Bytes)

## Slide 138: Address Resolution Protocol (ARP)

## Slide 139: Domain Name Service (DNS)
Resolves host names to IP addresses
Often occurs before malicious traffic
Also used for data exfiltration
Usually UDP 53
  Can be TCP 53

## Slide 140: DNS Query Header
https://technet.microsoft.com/en-us/library/bb962025.aspx

## Slide 141: DNS Response Header
https://technet.microsoft.com/en-us/library/bb962025.aspx

## Slide 142: DNS Recursion

## Slide 143: DNS Odd Behavior

## Slide 144: File Transfer Protocol
Plaintext protocol for transferring files
May be wrapped in SSL (FTPS)
Not to be confused with SFTP (SSH file transfer)
USER command to send username
PASS command to send password
Two types of FTP, active and passive

## Slide 145: Active Mode FTP
Client connects to server on port 21 (command channel)
Client gives server an ephemeral port for data (data channel)
Server connects back to client on data channel (ephemeral source and destination)

## Slide 146: Active Mode FTP

## Slide 147: Passive Mode FTP
Client connects to server on port 21 (command channel)
Server gives client an ephemeral port for data (data channel)
Client connects to server on data channel (source port 20)

## Slide 148: Passive Mode FTP

## Slide 149
Part 4 – Scapy

## Slide 150: Scapy
Python packet crafting library
Written by Philippe Biondi
Slow, but simple
  Not great for broad scanning
Helpful for simulating odd behavior
Allows complex sequences of packets

## Slide 151: Scapy
Define each layer of a packet
Ping localhost
  testpacket = IP(dst="127.0.0.1")/ICMP()
Connect to Bing on port 80 TCP
  testpacket = IP(dst=”www.bing.com”)/TCP(dport=80)/”GET / HTTP/1.1\n\n”
  Not going to work great
    Data on SYN
    Networking stack will reset the connection

## Slide 152: Scapy – useful commands
ls(): list all object members

## Slide 153: Scapy – useful commands
object.summary: list non-default field values

## Slide 154: Scapy – useful commands
Resp, noresp = sr(testpacket)
  Send packet, match responses. Store responses in resp, unanswered packets in noresp
sr1(testpacket)
  Send packet, match single response
send(testpacket)
  Send packet, do not look for responses

## Slide 155: Scapy – notes
Native networking stack may get confused
  Diagnose with tcpdump
  Use iptables to prevent it
  iptables --save >> iptables_original
  iptables –A OUTPUT –p tcp –tcp-flags RST RST –j DROP
    Fix using iptables --restore iptables_original or iptables --flush
Run Scapy as root

## Slide 156
Part 5 – Analysis Tips

## Slide 157: Common External Ports
Good egress filtering should block most external traffic
Permitted traffic should go through an intermediary
  TCP:80 (HTTP)
  TCP:443 (SSL)
  UDP:123 (NTP)
    Should be blocked
  UDP:53 (DNS)

## Slide 158: Common Internal TCP Ports
22 (SSH)
445 (SMB)
88 (Kerberos)
135 (DCE/RPC)
389 (LDAP)
636 (LDAPS)
993 (IMAPS)

## Slide 159: Common Internal TCP Ports
80 (HTTP)
443 (HTTPS)
8080 (Alternate HTTP)
8443 (Alternate HTTPS)
Ephemeral ports (RPC)

## Slide 160: Common Internal UDP Ports
53 (DNS)
5355(LLMNR)
123(NTP)
514(SYSLOG)

## Slide 161: Alerts
Many sources
  Intrusion Detection System
  Intrusion Prevention System
  Web Application Firewall
Signatures are not always great
Places to start
  Use the source port

## Slide 162: Continued Analysis
Work forward for post infection
  Find binary files for analysis
  Identify command and control traffic
Work backward to find the origin
  Often starts with legitimate sites

## Slide 163: Useful Techniques
Wireshark display filters
  dns || http.request.full_uri || ssl.handshake.certificate
Find “odd” URLs
  Long alphanumeric strings that are not words
  Directed outside of domain
  Use “referer” to work backwards
  Find redirection call in calling page (URL string)

## Slide 164: Automated Tools
Virustotal.com
  Binaries or pcaps
Sandboxes
  https://zeltser.com/automated-malware-analysis/

## Slide 165: More Training
https://malware.dontneedcoffee.com/
https://contagiodump.blogspot.com/
https://www.malware-traffic-analysis.net/
https://www.root-me.org/

## Slide 166
Part 6 – Practical Exercise

## Slide 167: ch2.pcap (from root-me.org)
Find the FTP password

## Slide 168: ch3.pcap (from root-me.org)
Find the twitter password

## Slide 169: 2015-03-24-traffic-analysis-exercise.pcap (from malware-traffic-analysis.net)
IP address of the infected host
Which server is probably legitimate, but compromised?
What redirection techniques does this exploit kit use?
What malware was used?

## Slide 170: sansholidayhack2013.pcap (from the SANS holiday hack challenge, 2013)
What are the MACs and IPs of the machines that ARP cache poison? Is it successful?
What are the IPs of the systems that were port scanning?
What systems and protocols did the scan discover?
What account was used in an attack over the SMB protocol?

## Slide 171: packet_intro.pcap
What are the max and minimum SSL/TLS versions supported by 192.168.2.122?
Find the 7 flags

## Slide 172
Part 7 – Practical Exercise Answers

## Slide 173: ch2.pcap
Find the FTP password
  ngrep for PASS

## Slide 174: ch3.pcap
Find the twitter password
ngrep -qI ch3.pcap 'Authorization: Basic' | tr ':' '\n' | grep 'Basic' | cut -f3 -d' ' | cut -f1 -d'.' | base64 –d

## Slide 175: 2015-03-24-traffic-analysis-exercise.pcap
IP address of the infected host
  192.168.122.200
Which server is probably legitimate, but compromised?
  forums.pelicanparts.com
What redirection techniques does this exploit kit use?
  Script tag injection
What types of exploits were served?
  Adobe Reader, Flash, Java, Silverlight

## Slide 176: sansholidayhack2013.pcap
What are the MACs and IPs of the machines that ARP cache poison? Is it successful?
  00:0c:29:f7:f4:9a - 10.21.22.253 - successful
  10.25.22.252 - unsuccessful
What are the IPs of the systems that were port scanning?
  10.25.22.252,10.21.22.253,10.25.22.253
  tcpdump -nn -r sansholidayhack2013.pcap 'tcp[13]=0x02' | cut -f3,5 -d' ' | tr ' ' '.' | cut -f1-4,6-10 -d'.' | sort | uniq -c | sort -rn
  tcpdump -nn -r sansholidayhack2013.pcap 'tcp[13]=0x14' | cut -f5 -d' ' | cut -f1-4 -d'.' | sort | uniq -c | sort -n

## Slide 177: sansholidayhack2013.pcap
What systems and protocols did the scans discover?
  tcpdump -nn -r sansholidayhack2013.pcap 'tcp[13]=0x12 && (dst host 10.25.22.252 || dst host 10.21.22.253 || dst host 10.25.22.253)' | cut -f3 -d' ' | sort | uniq

## Slide 178: sansholidayhack2013.pcap
10.16.11.5.110 | 10.25.22.22.80 | 165.254.158.56.80 | 208.80.154.234.80
10.21.22.22.502 | 10.25.22.23.80 | 173.194.43.47.443 | 208.80.154.240.80
10.21.22.23.502 | 10.25.22.250.80 | 192.190.173.45.80 | 216.22.25.175.80
10.21.22.24.502 | 10.25.22.30.80 | 192.204.3.75.80 | 54.230.49.239.80
10.21.22.253.1225 | 10.25.22.58.4444 | 199.7.57.72.80 | 63.245.217.36.80
10.2.2.2.8081 | 10.25.22.58.445 | 208.80.154.224.80 | 69.16.175.10.80
72.167.239.239.80 | 74.125.226.239.443 | 82.103.140.42.443 | 74.125.226.228.80

## Slide 179: sansholidayhack2013.pcap
72.21.195.198.443 | 74.125.226.242.443 | 10.25.22.22.44818
72.21.203.211.80 | 74.125.226.251.80 | 165.254.138.136.80
72.21.214.3.443 | 74.125.22.82.80 | 208.80.154.225.80
72.21.215.52.80 | 81.169.180.37.443 | 69.195.141.178.443
74.125.226.199.443 | 81.169.180.37.80 | 82.103.134.102.80

## Slide 180: sansholidayhack2013.pcap
What account was used in an attack over the SMB protocol?
  ernie

## Slide 181: packet_intro.pcap
What are the max and minimum SSL/TLS versions supported by 192.168.2.122?
  Max: TLS 1.2
  Min: TLS 1.0

## Slide 182: packet_intro.pcap

## Slide 183: packet_intro.pcap
Flag 1
  http.request.full_uri contains “flag”

## Slide 184: packet_intro.pcap
Flag 2
  ngrep -qI packet_intro.pcap ‘flag2’

## Slide 185: packet_intro.pcap
Flag 3
  ngrep -qI packet_intro.pcap 'flag3'

## Slide 186: packet_intro.pcap
Flag 4
  echo "flag" | base64
  ngrep -qI packet_intro.pcap 'ZmxhZ’
  ngrep -qI packet_intro.pcap 'ZmxhZ' | grep 'ZmxhZ' | tr -s ' ' | cut -f3 -d' ' | cut -f2- -d'=' | base64 -d

## Slide 187: packet_intro.pcap

## Slide 188: packet_intro.pcap
Flag 5
  echo "flag5" | xxd -ps
  ngrep -qI packet_intro.pcap '666c616735’
  printf "666c6167353a6436386663373231646133316565663932663565373939616466643534653139" | xxd -r -p

## Slide 189: packet_intro.pcap

## Slide 190: packet_intro.pcap
Flag 6
  tshark -r packet_intro.pcap -T fields -e icmp.type -Y 'icmp' | xargs printf '%x' | xxd -r -p

## Slide 191: packet_intro.pcap

## Slide 192: packet_intro.pcap
Flag 7
  tcpdump -r packet_intro.pcap -nnA 'icmp' | grep '\.\.' | cut -f4 -d'-' | grep -v '@\.\.\.\.\.\.z' | tr -d '\n'

## Slide 193: packet_intro.pcap

## Slide 194
www.directdefense.com